## Slide 1
IILM UNIVERSITY, GREATER NOIDA
School of Computer Science and Engineering
INTERNSHIP PRESENTATION
Low-Cost Three-Channel EEG-Based Mental
Fatigue Detection Using Machine Learning
STUDENT
Sanjeev Kumar
ENROLLMENT NO.
____________
PROGRAM & SEMESTER
B.Tech CSE, ____ Semester
ORGANIZATION
Svaarogyam Medical Devices Pvt. Ltd.

## Slide 2
ORGANIZATION
Svaarogyam Medical
Devices Pvt. Ltd.
“Self care made easier.”
Jaipur, Rajasthan Headquarters
About the Organization
H
Healthcare Technology
A healthcare technology company focused on developing accessible medical devices and health-monitoring solutions.
S
Self-Care Focus
Emphasis on affordable, self-care-oriented technology for everyday health monitoring.
M
My Role
Data Science & ML Intern in the Backend Developer track — applying ML techniques to physiological signal data.
I
Internship Duration
1 June 2026 – 15 July 2026, Remote, 10:00 AM – 5:00 PM (Mon–Fri).

## Slide 3
The Problem: Mental Fatigue Goes Unnoticed
Prolonged cognitive effort reduces alertness and decision-making — a real safety risk in healthcare, transport and industry.
Costly Hardware
Commercial EEG systems are expensive, bulky and complex — impractical for everyday use.
Unreliable Monitoring
Questionnaires and behavioural checks can't give continuous, unbiased, real-time feedback.
Heavy ML Models
Deep-learning approaches need large datasets and GPUs, ruling out low-cost, portable devices.
EEG in the 8–30 Hz range (Alpha & Beta bands) is a well-established, non-invasive marker of cognitive fatigue — the challenge is capturing it reliably on cheap, wearable hardware.

## Slide 4
Project Objectives
1
Design and build an affordable, portable three-channel EEG acquisition system.
2
Isolate the Alpha (8–13 Hz) and Beta (13–30 Hz) bands relevant to cognitive fatigue.
3
Extract frequency-domain and statistical features suited to lightweight ML models.
4
Train and compare Random Forest, XGBoost, LightGBM and SVM classifiers.
5
Validate with subject-independent Leave-One-Subject-Out Cross-Validation (LOSO-CV).
6
Deploy on an ESP32 microcontroller with sub-200 ms real-time inference latency.

## Slide 5
System Architecture
Three-channel EEG signal flows through acquisition, processing and classification stages.
1
Signal
Acquisition
Wet Ag/AgCl electrodes → AD620 amplifier (CMRR > 90 dB) → DRL noise reduction (20–30 dB) → TL072 conditioning → ADS1115 16-bit ADC
→
2
Processing &
Feature Extraction
4th-order Butterworth bandpass filter (8–30 Hz) → 2-sec windows, 50% overlap → 24 features/window (band power, Alpha/Beta ratio, statistics)
→
3
ML Classification
Random Forest / XGBoost / LightGBM / SVM → LOSO-CV validation → binary output (fatigued / alert) on ESP32, < 200 ms latency

## Slide 6
Methodology & Dataset
14
Healthy participants
(18–22 yrs)
83 Hz
EEG sampling rate
15,189
Total labeled windows
55:45
Class split
(non-fatigued : fatigued)
Validation Approach
Leave-One-Subject-Out Cross-Validation (LOSO-CV): trained on 13 subjects, tested on the 1 held-out subject, repeated across all 14 — ensuring the model generalises to unseen people, not just unseen windows. Feature normalisation uses training-fold statistics only, preventing data leakage.
Extracted Features (24 / window)
Alpha Band Power (8–13 Hz)
Beta Band Power (13–30 Hz)
Alpha/Beta Ratio
Mean & Standard Deviation
Skewness & Kurtosis
Peak-to-Peak Amplitude

## Slide 7
Model Performance
Random Forest was the best performer across all metrics.
Chart: Metric Comparison (%)
| Random Forest | XGBoost | LightGBM
Accuracy | 75.92 | 74.73 | 74.97
Precision | 84.91 | 80.73 | 81.85
Recall | 56.41 | 57.43 | 56.87
Model | F1 | AUC
Random Forest | 0.678 | 0.763
XGBoost | 0.671 | 0.752
LightGBM | 0.671 | 0.753
Reading the Numbers
High precision (84.9%): few false alarms — crucial for workplace trust. Moderate recall (56.4%): conservative model, misses some subtle fatigue onsets. Confusion matrix: 7,684 normal & 3,848 fatigued states correctly identified.

## Slide 8
Practical Trade-off vs. Deep Learning
A small accuracy gap buys a large drop in cost, complexity and power.
Parameter
Wang et al. (2023)
CNN + CWT
Proposed Work
ML Pipeline
Channels
Multi-channel (16+)
3-channel
Compute
GPU (≈ 0.5 TFLOPS)
MCU (≈ 0.0003 TFLOPS)
Feature Extraction
Automatic (deep)
Manual (Alpha/Beta + stats)
Accuracy
88.85%
75.92%
Real-time Latency
Moderate
< 200 ms
Cost & Complexity
High
Low, low-cost

## Slide 9
Key Outcomes
1
Working Prototype
Three-channel EEG hardware acquiring usable signals in the 10–100 µV range.
2
Validated ML Pipeline
Random Forest reaching 75.92% accuracy and 84.91% precision, subject-independent.
3
Real-Time on ESP32
Sub-200 ms inference latency at ≈ 45 mW power — wearable-ready.
4
Low-Cost Alternative
A practical, affordable substitute for high-density GPU-dependent EEG systems.

## Slide 10
Thank You
Questions & Discussion
Sanjeev Kumar
Data Science & ML Intern — Svaarogyam Medical Devices Pvt. Ltd.